## Slide 1: Optimizing CubeSat Attitude Control
Dmitriy Rivkin

## Slide 2: Reaction Wheel Control Scheme
Three flywheels mounted along body (x,y,z) axes
Actuated using brushless DC motors
Conservation of momentum: spin the wheels one way, the satellite spins the other way

## Slide 3: Reaction Wheel Advantages
No fuel burned (energy used is electrical)
High performance

## Slide 4: Optimization Objectives
1. Minimize time for large-angle slew
2. Minimize electrical energy consumed (final time fixed)

## Slide 5: Dynamic Model
System is modeled as four rotating rigid bodies
  3 wheels and 1 satellite body
  Centers of mass fixed w.r.t. overall center of mass
Control input is acceleration of reaction wheels (motor torque/wheel MOI)
Quaternion attitude representation

## Slide 6: Parameters of Optimized Problem
1u CubeSat
  10cm cube , 1kg
  MOI = 1.528 kg*mm
Wheel MOI = 0.101 kg*mm
  100g wheels, 90mm diameter
Satellite body is 10cm cube
  Uniform mass distribution
Motor torque
  3mNm (Faulhaber 2610b)

## Slide 7: Constraints
|Wheel acceleration| <30 rad/s2
  Comes from wheel MOI and motor torque
|Wheel speed|<630 rad/s
  Motor really will output full torque through the whole speed range if controlled appropriately

## Slide 8: Time Optimization
Large slew angle
Cost function = tf
Numerical solution obtained (N=50)
10 states
  wheels speeds, body rate, orientation
3 controls
  acceleration of each wheel

## Slide 9: Time Optimal Results: Path

## Slide 10: Controls
Clearly Bang-Bang

## Slide 11: Rotation Rates

## Slide 12: Hamiltonian Value Condition

## Slide 13: Hamiltonian Minimization Condition
Analytical derivatives computed using Matlab

## Slide 14: Discussion of Time Optimal Results
Lengthy computation
  About 5 minutes for N=16 no guess
Solution is sometimes not found for higher numbers nodes
  Have to “work your way up” by getting solutions for smaller numbers of nodes and using them as guesses
Not nice computationally because of discontinuous nature of solution

## Slide 15: Discussion of Time Optimal Results
Significant performance improvement over linear quaternion error feedback control law
  3.5s vs about 12s
Bang bang solution was expected

## Slide 16: Main Source of Energy Loss
CubeSats have severe energy limitations
When a wheel is spun up, electrical energy is converted into mechanical energy
This energy is not recovered when the wheel is spun down (dissipated as heat)
=

## Slide 17: Other Losses
Bearing friction )
Resistive losses ()
Switching losses
  Independent of speed or acceleration, although if you can turn the motors off you will certainly save here

## Slide 18: Issues with |power| Cost Function
I tried a number of schemes to smooth out the cost function.
  I think they were legitimate, but I did not get any reasonable looking solutions
Even didn’t work
  Definitely smooth
  DIDO didn’t seem to like states being multiplied by controls in the cost function

## Slide 19: Example of DIDO solution
N = 64
It’s bad

## Slide 20: What to do?
Eventually I gave up, and tried the cost function
Results!

## Slide 21: Min Solution, N=64

## Slide 22: Controls

## Slide 23: Satellite Body Rate

## Slide 24: HVC

## Slide 25: HMC

## Slide 26: Discussion
Bang – Off – Bang solution
  Accelerate as quickly as you can to a constant speed
  Stay at that speed until you have to stop
  Stop as quickly as possible
This solution minimizes frictional losses (which is nice)
This solution looks exactly like what I intuitively expected for the cost function

## Slide 27: Discussion
In one dimension, this control:
  Optimizes
  It also optimizes because each wheel only ever spins in one direction
How to check / prove if the solution optimizes ?
Why doesn’t DIDO work well for cost function?

## Slide 28: To Do
Optimize 3U CubeSat trajectories (30x10x10 cm)
  More likely to have this kind of controller
Suggestions?